## Slide 1
Smart Farm Monitoring System
Project By-
Vishwas Kapoor(12115020)
Vanshika Gandhi(12115037)
Tanisha Goel(12115069)
Project Mentor-
Dr. Ghanapriya Singh
Asst. Professor, ECE Dept.
NIT Kurukshetra

## Slide 2
Need for Smart Farming - THE MOTIVATION
  Traditional farming relies on manual soil inspection
  Leads to inefficient irrigation and water wastage
  Large farms have variable conditions across different zones
  Rural areas lack reliable internet and power
  Need for affordable, power-efficient, and remote monitoring solutions

## Slide 3
Objective of the Project
  Design a wireless system to monitor real-time temperature, humidity, and soil moisture
  Implement LoRa-based communication for long-range, low-power data transfer
  Focus on efficient power consumption using deep sleep mode and minimal transmissions
  Use a microcontroller as an edge device for local sensing and preprocessing
  Enable cloud access to data for farmers via a mobile application
Empowering a farmer with data is like giving them the power to predict the future—weather, water, and yield.

## Slide 4
Our Solution
We developed a Smart Farm Monitoring System that:
  Uses low-cost microcontrollers and sensors
  Transmits data via LoRa in remote areas without internet.
  Displays data on Blynk mobile app dashboard in real-time.
  Focused on low-power, long-range, and scalable design.

## Slide 5
System Architecture
}
  Wemos D1 Mini + Sensors (DHT11, Soil Moisture)
  SX1278 LoRa Module for wireless data transmission
  Powered by a 9V battery + voltage regulator
Transmitter Node (Field)
  NodeMCU + SX1278 LoRa Module
  Receives data and sends it to Blynk Cloud
  Data is viewed on the farmer’s smartphone app
Receiver Node (Base)

## Slide 6
Project Components
Sensors
01
04
  DHT11 Sensor
  Measures temperature and humidity
  Digital output, cost-effective for basic environmental sensing
  Capacitive Soil Moisture Sensor
  Detects soil moisture level
  Analog output, corrosion-resistant design
Communication Module
02
  SX1278 LoRa Module
  Enables long-range, low-power wireless communication
  Ideal for remote farm locations
  Power Supply
  9V Battery + LM7805 Regulator
  Suitable for outdoor/field deployment
Microcontrollers
03
  WeMOS D1 Mini
  Compact version of ESP8266, used in Wi-Fi-based testing
  NodeMCU ESP8266
  Main controller for both transmitter and receiver nodes
  Built-in Wi-Fi, low-power, Arduino-compatible

## Slide 7
Hardware Setup
The setup uses the WeMos D1 Mini as the transmitter, connected to the DHT11 and soil moisture sensor, powered through a 9V battery regulated to 5V. It collects sensor data and sends it via its SX1278 LoRa module to the NodeMCU receiver, which is also connected to an SX1278 module and forwards the data to the cloud

## Slide 8
Pin Connections
  The SPI pins (MISO, MOSI, SCK) connect NodeMCU and LoRa to exchange data.
  NSS (Chip Select) tells the LoRa module when the NodeMCU wants to communicate.
  RESET lets the NodeMCU reset the LoRa module if needed.
  DIO0 is an interrupt pin signaling when transmission or reception is done.
  VCC powers the LoRa module with 3.3V from the NodeMCU.
Component | Pin on NodeMCU | Pin on SX1278 LoRa Module
MISO | D6 (GPIO12) | MISO
MOSI | D7 (GPIO13) | MOSI
SCK | D5 (GPIO14) | SCK
NSS (CS) | D8 (GPIO15) | NSS (Chip Select)
RESET | D0 (GPIO16) | RESET
DIO0 (Interrupt Pin) | D1 (GPIO5) | DIO0
VCC | 3.3V | VCC

## Slide 9
Working of LoRa Communication in Our System
  LoRa is a long-range, low-power wireless communication technology.
  It uses Chirp Spread Spectrum (CSS) modulation, where signals “chirp” by sweeping frequencies across a wide bandwidth.
  CSS helps LoRa to be highly resistant to interference and enables long-distance communication with low power.
  Network Components:
Sensors: Collect and send data wirelessly.
Gateways: Receive and forward sensor data.
Network Server: Routes and manages data.
Application Server: Processes data for users.
  Data Flow:
Sensor → Gateway → Network Server → Application Server → User

## Slide 10
1. Deep Sleep Mode
  Microcontroller enters low-power sleep state between readings.
  Significantly reduces idle power usage in field deployment.
Innovative Approach for Power Consumption
2. Threshold-Based Transmission
  Data is only transmitted when critical values are detected:
  e.g., Low soil moisture or high temperature
  Reduces unnecessary wireless communication and power drain.
3. Scheduled Sensing
  Sensors collect data at fixed intervals (e.g., every 10–15 minutes).
  Balances data accuracy with energy efficiency.

## Slide 11
Future Scope
1. Automated Irrigation System
  Integrate water pumps controlled by sensor data.
  Enable automatic irrigation based on soil moisture levels.
2. Solar-Powered Deployment
  Replace batteries with solar panels for sustainable power.
  Ensure uninterrupted operation in remote areas.
3. Web Dashboard Integration
  Develop a centralized platform for large-scale farm monitoring.
  Real-time access via desktop and mobile.
4. Expandable Sensor Network
  Add sensors for:
Soil pH, light intensity, rainfall, CO₂
  Enable a more complete picture of field conditions.

## Slide 12
THANK YOU